## Slide 1
IronGate SW Architecture Proposal
AR&VR Team

## Slide 2: Agenda
Hardware Architecture Brief
Software Architecture
  Software architecture
  HMD software high level design
  EPU software high level design
  Power on/off
  Power saving

## Slide 3
Dual Display
DP
Sub Battery
HMD
DP over USB-C
Hardware Architecture
USB3.0
DP Bridge
SD835
RGB Camera
6Dof RGB Camera
MIPI
MIPI
Sensor Hub (IMU L&P Sensors)
SPI
Audio Codec
Mic & Speaker
SLIMBUS
Depth Camera
MIPI
Voice Wakeup
I2S/INT
Type C
EPU
Phone
PC
EPU/Phone/PC

## Slide 4
Dual Display
DP
Sub Battery
HMD
DP over USB-C
HW Architecture w/ EPU Design
USB3.0
DP Bridge
SD835
RGB Camera
6Dof Camera
MIPI
MIPI
Sensor Hub (IMU L&P Sensors)
SPI
Audio Codec
Mic & Speaker
SLIMBUS
Main Battery
EPU
SD835
BT&WIFI&4G
GPS
QLink
WIFI I/Q..
SPI
HDMI out
Depth Camera
MIPI
Sensor Hub (IMU Sensors)
Voice Wakeup
I2S/INT
Type C

## Slide 5: Software Architecture
HMD is a peripheral of console (EPU/PC/Phone), w/ very powerful CAM, CV & Audio capability.
Standard USB protocol is used between HMD & console. Console(no extra driver needed) is a USB host device, and HMD is a composite USB device w/ CAM, IMU, Spkr, Mic…..
Architecture is similar to Klamath & other tethered helmet (OC CV1, LG 360 VR)
USB Host
USBH Camera
USBH Audio
USBH HID
Games
DP Out
APP
Launcher
AR SDK 3D Engine Plugin Client
Settings
Air Suite
OpenGL/D3D/Vulkan
DP In
USB HUB / Composite device
Sensors Algorithm
USB Camera
USB Audio
USB HID
HMD
ISP(RGB camera)
HMI Sensors(Depth/6Dof/IMU)
Dual Display
Other Apps
AR SDK Runtime
AR Input(Virtual Mouse & Key)
AR NDK
System Standard SDK & Libraries
Customized Apps
AR SDK Native Client
EPU
System

## Slide 6: HMD SW Architecture (w/ System functions)
USB Composite device
DP
Depth
Sensor
Display
ISP
USBD Audio
USBD Camera
USBD HID
Audio
Codec
PM
Linux Kernel
KEY
LED
9 Axis
IMU
P/L Sensor
Gesture
Algorithm
6Dof
Algorithm
IMU Fusion Algorithm
Battery
DDR
UFS
BOOTLOADER
6Dof Sensor
USB 3.0 HOST TO PCIE
OTA
Atheer, Customized
Flex AR&VR, Customized
Flex non-AR&VR, Customized
Android Standard
Featured
Algorithm

## Slide 7: EPU SW Architecture (w/ System functions)
AR NDK
TF
USB Host
DDR
UFS
PM
HDMI
Battery
BT
WIFI
Air Setting
KEY
LED
Game Apps(Use Game Engine Plugin)
Android Standard SDK
BOOTLOADER
DP
EPU Sensor
HUB
USBH Camera
USBH Audio
USBH HID Sensors
IMUs/Gestures/6Dof
Sensor HAL
ALSA / Camera
GPS
Stereo Rendering
Multimedia
Framework
Graphic
Front Buffer Rendering
USB 3.0 HOST TO PCIE
USB CDC
Modem
RIL
Atheer, Customized
Flex AR&VR, Customized
Flex non-AR&VR, Customized
Android Standard
OTA
AR SDK
Android 2D Apps
Launcher(with Voice Recognition Command)
Air suite
Others Apps
Touch Screen Virtualization

## Slide 8
  Customized Android system for AR devices
    Customized Android Launcher and interaction method to create advanced user experience
    Compatible classic 2D application using Gestures and Gaze input interaction method.
  Algorithm for 3D Gestures
    Supports 3D gestures to replace the touch pad & keyboard.
  Algorithm for 6DoF
    Supports precision gaze input and head motion tracking.
    Supports 6DoF position tracking.
  Algorithm for Voice wakeup and Voice command
    Supports voice wakeup and voice command using multi-mic.
  Provide Unity & Unreal engine plugin
    Supports using unity & unreal to create 3D apps/games.
Software Key Features

## Slide 9: NDK and SDK
Flex AR NDK provide uniform APIs for hardware access:
  APIs for depth sensor;
  APIs for dual 9 axis IMU sensor;
  APIs for stereo fisheye camera;
  APIs for voice wakeup chip.
Flex AR SDK provide friendly user interface:
  APIs for 6DoF, including 3DoF pose and 3DoF position;
  APIs for gesture command;
  APIs for voice wakeup customization and voice command;
  Unity and Unreal engine plugin to support using unity & unreal create 3D apps/games.
With IronGate powerful hardware/system support, customer can use our AR NDK/SDK to develop their application with good flexibility. E.g. use the low level NDK to develop their own AR featured algorithm, and directly use key algorithms we integrated in the high level AR SDK. And we can use the powerful SD835 to migrate & optimize AR related framework, such as OpenCV, ARToolkit, etc.

## Slide 10: Factory production related
Download tool
Function test tool
Calibrations tools
  9 Axis IMU sensor calibration, Gyro, Mag, Acc
  Stereo 6DoF camera
  Light engine alignment
  Hand Gesture calibration

## Slide 11: Power On/Off
EPU Android
Power on
HMD Android
Power on
USB Power 5V Available
EPU Android
Power off
HMD Android
Power off
USB 5V Not Available
Power Key On EPU
Power Key Off EPU
HMD Android
Resume
EPU Android
Resume
EPU Sleep USB Attach
USB Attach
HMD Android
Sleep 30 Seconds Then Power off
EPU Android
Sleep 30 Seconds Then Power off
USB Detach

## Slide 12: Power Saving
HMD Android
Resume
EPU Android
Resume
Near Proximity sensor High Interrupt
Voice wakeup Interrupt
USB Remote Wakeup
HMD Android
Sleep
EPU Android
Sleep
USB Suspend
Near Proximity sensor Low Interrupt
HMD Gesture
Off
Far Proximity sensor Low Interrupt
HMD Gesture
On
Far Proximity sensor High Interrupt

## Slide 13: Thank you! Q & A
Q & A