## Slide 1
IronGate QVR Service Discussion
AR&VR Team

## Slide 2
Dual Display
DP
Sub Battery
HMD
DP over USB-C
HW Architecture w/ EPU Design
USB3.0
DP Bridge
SD835
RGB Camera
6Dof Camera
MIPI
MIPI
IMU BMW055
SPI
Audio Codec
Mic & Speaker
SLIMBUS
Main Battery
EPU
SD835
BT&WIFI&4G
GPS
QLink
WIFI I/Q..
SPI
HDMI out
Depth Camera
MIPI
IMU BMW055
Voice Wakeup
I2S/INT
Type C

## Slide 3: Software Architecture
USB Host
USBH Camera
USBH Audio
USBH HID
Games
DP Out
SDK
APP
Launcher
Game Engine Plugin
Settings
Other Apps
QVR service
DP In
USB HUB / Composite device
USB Camera
USB Audio
USB HID
EPU
OS
HMD
Dual Display
IMU(BMW055)
QVR service(with 6DoF)
IMU
BMW055
Dual 6DoF Sensor
6DoF Data
Decode 6DoF Data
HMD has one IMU sensor and stereo 6DoF camera, these sensors data fusion by QVR service in HMD, then sending the 6DoF information to EPU via USB HID, there is a IMU sensor in EPU also, data fusion by QVR service in EPU, application can alternative use these two kinds of pose data which produced by EPU(output by QVR service in EPU) and HMD(output by QVR service in HMD).
HMD system no display out, dual display video frames comes from EPU directly via DP.
AR SDK
Air Interaction
AR NDK
Android Standard SDK

## Slide 4: QCT QVR service

## Slide 5: Question
Q1: Can QVR service in HMD supports system without display?
Q2: Pose output by HMD QVR service, transmit to EPU, and application in EPU uses this pose data for rending, is there a risk of sensor latency?
HMD sends the following data to EPU at the same time:
USB camera data stream, 1080P @ 30fps.
USB audio data stream, e.g., 44.1khz @ 2ch.
USB HID data stream, including 3DoF/6DoF information.