## Slide 1
Hardware Architecture
Flex AR&VR Team

## Slide 2: Hardware solution(HMD+EPU)
USBC Cable
Head Mounted Display
Belt Pack (External Processor Unit embedded)
Solution: One SD835 (Android) in HMD(Head Mounted Device), another SD835 (Android) in Belt Pack. Belt Pack SD835 serves as application processor, and HMD SD835 serves as co-processor for audio, image, video, CV, IMU sensors, etc, like HPU in HoloLens.

## Slide 3: IronGate Hardware Description
 | HMD | EPU
CPU | APQ8098 | APQ8098
DDR Memory | LPDDR4X 4GB(may use 2GB to make cost effective) | LPDDR4X 4GB
UFS/EMMC | UFS 32GB | UFS 64GB(Extensible to 128GB)
RGB Camera | Still capture 12M, Auto Focus; Video 1080p@30fps | 
Depth Camera | TOF | 
6DOF Camera | Stereo,720p | 
IMU | 9-Axis | 9-Axis
Ambient Light Sensor | Yes | 
Proximity Sensor | Yes | 
Display | top-down projection, binoculars, 720p@60fps | 
Audio | 4Mics+2Spks | 
Voice wakeup | Yes | 
3.5mm Phone Jack | Yes | 
GPS |  | Yes
BT+WiFi |  | BT 4.0 above; WIFI (802.11 b/g/a/n/ac 2.4G/5G)
4G LTE |  | Yes
USBC | Yes | Yes
HDMI2.0 |  | Yes
Battery | 500mAh | 10000mAh
Charging |  | QC3.0

## Slide 4
APQ8098Lite
RGB Camera
Depth Camera
UFS-32GB
MIPI-4Lane
MIPI-2Lane
UFS
DP
Sub_Battery
HMD
Hardware Architecture Solution - HMD
USB3.1 Gen1
DP Bridge
9-Axis Sensor
ALS/PS Sensor
SPI/I2C
LPDDR4X-PoP
PMI8998/PM8998/PM8005
I2C
PWR
WCD9341
Voice Activation
SLIMBUS
Mic1/2/3/4
2xWSA8815
USB_5V
button
Status LED
USBC Switch and CC logic
USB 3.0 To PCIe Bridge
PCIe
6DOF Left Camera
MIPI-1Lane
USBC
2xSpk
Headphone
Flash LED
dlp3433
dlp3433
DLPA2005
Opt Engine+ DMD
DLPA2005
Opt Engine+ DMD
DLP Board
6DOF Right Camera
MIPI-1Lane
USBC
EPU

## Slide 5
APQ8098
UFS 64GB
WiFi/BT
GPS LNA
UFS
I/Q
Qlink
DP-2lane+ USB3.1Gen1
EPU
Hardware Architecture Solution – EPU
LPDDR4X PoP
T-Flash
PMIC
Main_Battery
I2C
PWR
9-Axis IMU
5V
WTR 5975
BT UART
Chain1
Chain0
ANX7426 USBC Switch and CC logic
Micro USB2.0 OTG
HDMI
USB2.0
PCIe
4G LTE Module(option)
Status LED
Button
USB 3.0 To PCIe Bridge
DP2Lane
Usb3.0+2.0
5V Boost
Current limit Reverse block
VPH_PW
HDMI OUT
USBC1
USBC2
Slimbus
USB2.0/3.0
Usb2.0/3.0
Diplexer
QC3.0 charger /USB2.0 expansion
Usb2.0
USB2.0
HMD
5V

## Slide 6: Voice Wake up and Recognition
WCD9341
Sound Classification, Keyword detection & user validation
Initial audio detection
Audio subsystem LPASS (QDSP6)
Apps Processor
SVA Framework
OEM Application
APQ8098
voice activation algorithm runs on the codec to minimize power
voice activation algorithm runs on AP
Support two methods:

## Slide 7: Expansion in future
2. Mobile +HMD
3. PC/Laptop+HMD

## Slide 8: The End