## Slide 1: Case 1:Default state(Power off + plug in)
Enter boot
PMI8998 power up
Initialize ANX7325
USB-PD Logic on CC1/CC2
ANX7325 Generates an interrupt and the source supports 3A
Exception state
Change PMI8998 input current to 3A in boot code
Power off
USB plug in
N
Y
Boot to Linux

## Slide 2: Case 2: Default state(Power on + unplug)
Power on and Linux/Android system running
Change PMI8998 input current to 900mA in USB hot plug event handler
USB unplug

## Slide 3: Case 4: Default state(Suspend + plug in)
Suspend
USB plug in
USB-PD Logic on CC1/CC2
ANX7325 generates an interrupt and source supports 3A
Exception
AP is waked up by ANX7325
Change PMI8998 input current to 3A in resume code
N
Y

## Slide 4: Case 4: Default state(Suspend + unplug)
suspend
USB unplug
AP is waked up by ANX7325
exception
Change PMI8998 input current to 900mA in resume code
N
Y

## Slide 5: Notes
Change the input current limit using the following procedure: i) Configure 0x1370 to the desired input current limit ii) Configure 0x1365[4]=1, 0x1341[1]=1 (allows SW to over-ride input current limit based on 0x1370)