## Slide 1
IronGate Display Requirement on EPU BSP
Donny Tang
May 2nd. 2018

## Slide 2: IronGate Display Background
IronGate Display HW
  IronGate POC HMD has two 720p light engines – OE33
  IronGate EVT HMD has two 1080p engines - Vision
  The engines are connected to EPU SD835, thru DP over USB-C
  There’s an HDMI extension port on EPU
EPU Display Software Basic Goals
  Support both HMD & HDMI extension simultaneously
  Support both POC & EVT HMD, and switch resolution automatically

## Slide 3: SW Requirement to EPU BSP #1
Always set DP port (HMD) as primary display, regardless whether there’s a DP display connected; set HDMI port as secondary display, if detected
Set EPU primary framebuffer according to the HMD display EDID resolution respectively
    720p engine -> frame buffer 2560 x 720
    1080p engine -> frame buffer 3840 x 1080
Set secondary frame buffer according to HDMI display EDID resolution detected, including …… (we need a set of resolutions here)
No need to define secondary frame buffer if no HDMI display detected

## Slide 4: SW Requirement to EPU BSP #2
Debug Mode
    Set EPU primary framebuffer to 3840 x 1080 for App development without HMD, if there’s no DP display detected
    Set EPU primary framebuffer to 3840 x 1080 for App development, if a normal 16:9 or 4:3 LCD monitor is detected on DP port (over USB-C)

## Slide 5
END

## Slide 6
HW Architecture w/ EPU Design
Dual Display
DP
HMD
DP over USB-C
USB3.0
DP Bridge
SD835
EPU
SD835
HDMI out
Type C